Save This Manual For Future Reference

MODEL NUMBER :   CM500

SERIAL NUMBER:

FOR YOUR SAFETY

READ AND UNDERSTAND THE ENTIRE MANUAL BEFORE OPERATING MACHINE

TABLE  OF  CONTENTS

Specifications Table…………………………………..2

Safety Warnings & Instructions……………………..3

Contents of the shipping container………………….6

Assembly Instructions………………………………..7

Operation Instructions……………………………….9

Maintenance Instructions……………………………10

Parts Schematic………………………………………11

Parts List…………………………………..……….....12

SPECIFICATIONS    TABLE

| Item | Description |
| --- | --- |
| Motor | P1=4KW S6 40% |
| Voltage | 380V |
| Frequency | 50Hz |
| Drum Capacity | 500L |
| Drum Mouth | 500mm |
| Drum Speed | 30rpm |
| Overall Sizes | L | 2400mm |
|  | W | 2090mm |
|  | H | 1740mm |
| Weight | 344Kg |

SAFETY WARNINGS AND INSTRUCTIONS

- UNDERSTAND YOUR MIXER

Read and understand the owner’s manual . Learn its application and limitations as well as the specific potential hazards peculiar to it.

Become familiar with the controls before operating this mixer.

- STAY ALERT

Do not operate the mixer while under the influence of drugs, alcohol, or any medication that could affect your ability to use it properly.

Do not use this mixer when you are tired or distracted from the job at hand. Watch what you are doing at all times. Use common sense.

- DRESS PROPERLY

Do not wear loose clothing, gloves, neckties or jewelry (rings, wrist watches). They can be caught in moving parts. Protective electrically non-conductive gloves and non-skid footwear are recommended when working. Wear protective hair covering to  contain  long  hair,  preventing  it  from  getting  caught  in machinery. Wear a face or dust mask if the operation is dusty. Always wear safety goggles and/or face shields. Everyday eyeglasses have only impact resistant lenses. They are not safety glasses

- AVOID  DANGEROUS  CONDITIONS

Make sure there is adequate surrounding workspace.Keep your work area clean and well lighted. Cluttered areas invite injuries. Keep area around the mixer clear of obstructions, grease, oil, trash and other debris which could cause persons fall onto moving parts.

Only use or operate the mixer on solid, flat, level ground that is capable to support the weight of the mixer and its load to prevent the mixer from tipping over.

Do not attempt to move the mixer when it is loaded and/or in operation.

This mixer is intended for the production of concrete, mortar and plaster. It is not suitable for the mixing of flammable or explosive substance.

- KEEP VISITORS AND CHILDREN AWAY

Keep unauthorized persons away from the mixer.

Do not allow children to handle or climb on or in the mixer.

- INSPECT YOUR MIXER

Check your mixer before turning it on. Keep guards in place and in working order. Check all bolts, nuts, and screws for tightness before each use, especially those securing guards and drive mechanisms. Vibration during mixing may cause these to loosen.

Form a habit of checking to see that all the adjusting tools, shovels, hand trowels and other tools/equipments are removed from mixer area before turning it on.

Replace damaged, missing or failed parts before using it.

- AVOID INJURY FROM UNEXPECTED ACCIDENT

Keep hands out of the way of all moving parts. Do not place any part of your body or any tool in the drum during operation. When operating, do not pass hands through the clearance between frame and support arm or the one between the drum and support arm.

- DO NOT FORCE TOOL

It will do a better and safer job at its design rate. Always work within the rated capacity.

Do not start the motor if the drum is fully loaded. Do not turn mixer off while full of concrete.

Do  not  use  the  mixer  for  a  purpose  for  which  it  was  not intended.

The mixer is not to be towed by any vehicle.

- DO NOT ABUSE CORD

Never carry mixer by cord or yank it to disconnect it from socket.

Keep cord from heat, oil and sharp edges.

- EXTENSION CORDS

Extension cords must be no longer than 50 meters in length. The wire section must be 1.5m㎡ on 400V to allow sufficient current flow to the motor. Improper use of extension cords may cause inefficient operation of the mixer which can result in overheating and motor damage.

Only extension cords to H07RN-F specification intended for outdoor purpose  may  be  used.  Avoid use  of  free  and inadequately insulated connections. Connections must be made with protected material suitable for outdoor use. Make sure that any extension cord connections are dry and safe. Ensure that the extension cord is carefully laid out avoiding liquids, sharp edges and places where vehicles might run over it. Avoid allowing the extension cord to be trapped underneath the mixer. Unroll it fully or it will overheat and could catch fire.

- NEVER LEAVE MIXER RUNNING UNATTENDED

Do not leave mixer until it has come to a complete stop.

- AVOID ELECTRICAL SHOCK

Check that the electric circuit is adequately protected and that  it corresponds with the power, voltage and frequency of the motor.

Do not plug or unplug the mixer while standing in or around damp or wet ground. Do not use the mixer in wet or damp areas or expose it to rain.

Make sure your fingers do not touch the plug’s metal prongs when plugging or unplugging the mixer.

- MAINTAIN YOUR MIXER WITH CARE

Clean the mixer immediately after use. Keep the mixer clean for best and safest performance.

When maintaining this mixer, only the manufacturer’s original replacement parts may be used.

- PROTECT THE ENVIRONMENT

Take left over materials to an authorized collection point or follow the stipulations in the country where the mixer is used. Do not discharge into drains, soil or water.

- STORE IDLE EQUIPMENT

When not in use, the mixer should be stored in a dry location to inhibit rust. Keep the mixer away from children and others not qualified to use it.

CONTENTS OF THE SHIPPING CONTAINER

BOLTS  AND NUTS  IN  BAG  TO  BE  USED  DURING  ASSEMBLY

ASSEMBLY  INSTRUCTIONS

NOTE :A shop crane may be needed during the assembly, Or more than three people  are  recommended  in  assembly.

THE   SUPPORT  LEG

Take down the 4 Support leg bolts which was inserted in The Main Frame. Lift the frame then insert the Support leg bolts with the end hole of the support leg align with the hole on the frame. Insert the pin to lock the bolt.

Then the other 3 legs and bolts in turn.

THE  AXLE  AND  WHEEL

Attach the axle and wheel assembly to the main frame as shown, Insert 2 bolts M14X80 from inside, then lock nut from outside. Tighten them. Then the other axle and wheel in the same manner.

LOAD  THE  WHEEL

When you moving the mixer, The wheel must be loaded, Lift the main frame by the side near the wheels, then recover the legs to the original position.

Mixing  Blade

Insert 2 bolts M10X25 through the holes  from outside of the lower drum, Then leather washer、 Mixing bade 、Lock nut M12 from inside. Secure the nut loosely.

Fix the other two mixing blades in the same manner.

NOTE:The leather washer should be placed between the blade and the drum.

UPPER  DRUM

Position the rubber gasket over the lower drum with the holes align.

Raise the upper drum and rotate it to the position as shown, Lay it against the rubber gasket with the holes align as before.

Insert 12 bolts M8X20 into each mounting holes on the rim, Secure each bolt from below with 12 Lock nuts.

Secure the upper drum and the mixing blade with 6 bolts M10X25 and lock nuts, Make sure the leather washer was placed  between  the blade and the drum.

Make sure the tightening process  is carried out  progressively.

TRACTION

Insert the traction，Secure  it  with a bolt M12X90 and a lock nut.

Operation Instructions

- Place the concrete mixer on a solid, flat, and level surface that is capable of supporting the weight of  the mixer and it’s load.

- Completely unwind the extension cord. Connect it to the concrete mixer first before plugging in power supply.

- Checking to see that all the adjusting tools, shovels, hand trowel and other tools/equipments are removed from mixer area ,Run the mixer, Grasp the tipping wheel and step on the pedal, Then rotate the  tipping wheel to adjust the drum mouth to a proper position. Loosen your foot, Let the plunger rod engage into the locking plate on the tipping wheel.

- For best results, proceed as follows:

  - Add the required amount of gravel into the drum.

  - .Add the required amount of cement into the drum.

  - Add the required amount of sand into the drum.

  - Pour the required amount of water into the drum.

- Allow adequate time for the water, gravel, cement and sand to thoroughly mix.

- To discharge the concrete mix, Grasp the tipping wheel firmly with your hand and step on the pedal to disengage the plunger rod , Then slowly turn the tipping wheel to empty the drum.                NOTE: Do not turn off the mixer while full of load, Emptying the drum with drum rotating.

- After discharging the concrete mixer, Rotate the tipping wheel in opposite direction to return the drum to its original position.

- Repeat  steps  3-7  if  more concrete is required

- Thoroughly clean the mixer at the end . The slightest trace of material left in the drum will harden and attract more each time you use it until  the  machine  is  useless.  Dried cement should be scraped out of the drum. Do not throw bricks into mixer drum to clean it out. Do not beat on the drum with a shovel, a hammer or other tools to break up accumulations of dried cement mix, As damage to the mixer may result. The drum may be scoured for approximate 2 minutes by gravel and water mixture. Then discharge the gravel/water mixture and hose down the drum assembly inside and outside

NOTE: Do not pour or spray water directly over the motor cover assembly especially the motor and the switch etc.

MAINTENANCE   INSTRUCTIONS

- CAUTION:  Do not perform any services or maintenance on the concrete mixer while it is running.

- Before each use, Inspect the general condition of the concrete mixer. Check loose screws, loose V-belt, binding of moving parts, loose or broken parts and other condition that may affect its safe operation. If it appears abnormal noise or vibration , Turn off the concrete mixer immediately and solve the problem before further use .

- Retighten the v-belt after the first 24 hours of use.

- Neither the manufacturer nor distributor makes any representation or warranty to the buyer that he or she is qualified to make any repairs to the product. The buyer assumes all risk and liability arising out of his or her repairs to the original product or replacement parts.

- When maintaining this mixer, only the manufacturer’s original replacement parts may be used.

PARTS      SCHEMATIC

| PARTS LIST |
| --- |
| part # | Description | Qty | part # | Description | Qty |
| 1 | Support Leg | 4 | 43 | sleeve Φ25 | 1 |
| 2 | Bolt M14*80 | 4 | 44 | Bearing 6205 | 6 |
| 3 | Lock Nut M14 | 4 | 45 | Side Gear Guard | 2 |
| 4 | Flat Washer 14 | 1 | 46 | Bearing Block - Right | 1 |
| 5 | pedal | 1 | 47 | Circlip 25 | 1 |
| 6 | Axis of rotation | 1 | 48 | Bolt M8*16 | 3 |
| 7 | Plunger Rod | 1 | 49 | Screw St3.5*13 | 4 |
| 8 | Spring | 1 | 50 | Switch Mount plate | 1 |
| 9 | cotter pin 5*40 | 2 | 51 | Lock Nut M6 | 2 |
| 10 | Flat Washer 16 | 1 | 52 | Switch | 1 |
| 11 | Tipping wheel | 1 | 53 | Idle Pulley | 1 |
| 12 | Little Gear | 1 | 54 | Screw M8*12 | 1 |
| 13 | sleeve Φ30 | 1 | 55 | Motor Cover assembly | 1 |
| 14 | Plastic sleeve Φ30 | 2 | 56 | Key 6*50 | 1 |
| 15 | Bearing Block - Left | 1 | 57 | Belt | 2 |
| 16 | Circlip 60 | 1 | 58 | Screw M5*45 | 2 |
| 17 | Bolt M12*30 | 6 | 59 | Lock Nut M8 | 16 |
| 18 | grease cup M10*1 | 2 | 60 | rubber handlebar | 2 |
| 19 | Steel Gear Cover | 1 | 61 | Lock Nut M5 | 2 |
| 20 | Screw M6*12 | 9 | 62 | Drive pulley | 1 |
| 21 | Key 6*20 | 1 | 63 | Key 6*50 | 1 |
| 22 | Circlip 30 | 1 | 64 | Screw M6*8 | 1 |
| 23 | Big Gear | 1 | 65 | Motor | 1 |
| 24 | Support Arm | 1 | 66 | Lock Nut M10 | 20 |
| 25 | Drive pinion | 1 | 67 | Motor Mount Bracket | 1 |
| 26 | Big cogwheel | 1 | 68 | Flat Washer 10 | 12 |
| 27 | Adjust Washer | 5 | 69 | Hubcap | 2 |
| 28 | Rubber Gasket | 1 | 70 | Flat Washer | 2 |
| 29 | Bearing 30212 | 2 | 71 | Wheel | 2 |
| 30 | Screw M10*25 | 12 | 72 | Hub | 2 |
| 31 | leather Washer 10 | 12 | 73 | DustProof Cover | 2 |
| 32 | Mixing Blade | 3 | 74 | Axle | 2 |
| 33 | Support Shaft | 1 | 75 | Support Leg Bolt | 4 |
| 34 | Bearing Cover | 1 | 76 | Bolt M10*25 | 8 |
| 35 | Upper drum | 1 | 77 | Bolt M8*25 | 4 |
| 36 | Lock Pin 10*60 | 1 | 78 | Pin | 5 |
| 37 | Bolt M12*40 | 17 | 79 | Main frame | 1 |
| 38 | Bolt M8*20 | 12 | 80 | Lock Nut M12 | 11 |
| 39 | dustproof Cover | 1 | 81 | Bolt M12*90 | 1 |
| 40 | Lower drum | 1 | 82 | Bolt M16*30 | 1 |
| 41 | O-ring 70*3.5 | 1 | 83 | Flat Washer 75 | 1 |
| 42 | Drive Shaft | 1 | 84 | Traction | 1 |